Quantum information presentation
Maximal Quantum cloning
Joseph Touzet

---
What are we trying to do ?
What are we trying to do ?
Using quantum teleportation as a universal primitive to unitary quantum gates
Typical universal set of quantum gates: {CNOT, X, Y, Z, H}

---
Quantum teleportation
Quantum teleportation
1 - The teleportation setup

---
Quantum teleportation
Quantum teleportation
1 - The teleportation setup

---
Quantum teleportation
Quantum teleportation
1 - The teleportation setup

---
Quantum teleportation
Quantum teleportation
2 - Why use quantum teleportation ?
- Use different types of qubit for computation and storage
- Long range qubit transportation

---
Using quantum teleportation to build quantum gates
Using quantum teleportation to build quantum gates
3 - From a quantum teleporter to the CNOT gate:

---
Using quantum teleportation to build quantum gates
Using quantum teleportation to build quantum gates
3 - From a quantum teleporter to the CNOT gate:
Using the CNOT gate we have built, and single-qubit gates we have a universal set of quantum gates !
Circuit functionality is proven later on

---
Fault tolerant quantum gates
Fault tolerant quantum gates
4 - introducing fault tolerance
Redondance block to correct faults
 -> Avoid operations within blocks to avoid error propagation
 -> Prefere transversal operations

---
Fault tolerant quantum gates
Fault tolerant quantum gates
4 - introducing fault tolerance: building gates from the C3 group
C1 and C2 gates can be applied transversely, while C3 gates cannot in general.

---
Fault tolerant quantum gates
Fault tolerant quantum gates
4 - introducing fault tolerance: building gates from the C3 group

---
Fault tolerant quantum gates
Fault tolerant quantum gates
4 - introducing fault tolerance: building gates from the C3 group

---
Fault tolerant quantum gates
Fault tolerant quantum gates
4 - introducing fault tolerance: building gates from the C3 group
We can build gates from the C3 group (Cn) only by applying gates from the C2 group (Cn-1) to the actual Qubits !
Can also be used to prove the CNOT gate circuit

---
Conclusion
Conclusion
Advantages of this method:
Typical advantages of quantum teleportation:
  - Apply gates on “volatile qubit”, while storing “stable qubit”
- Use already existing quantum teleportation device
- Apply “complex” gates (for fault tolerant comp.) using “simpler” gates